## Slide 1
OWEN EDWARDS
TRICS CONSORTIUM
LOCATION TYPE TRIP RATES
VARIATION IN TRICS

## Slide 2
OWEN EDWARDS
TRICS CONSORTIUM
Often brought up by users requesting guidance on trip rates survey samples
TRICS has undertaken an analysis to feed into an update on our guidance for users

## Slide 3
OWEN EDWARDS
TRICS CONSORTIUM
New research began in 2018, looking at regional trip rates variation
Current research in 2019 has looked at location type trip rates variation
A technical note will be produced later this year to cover both aspects

## Slide 4
OWEN EDWARDS
TRICS CONSORTIUM
2018 research indicated no evidence for fundamental direct influences on trip rates, with only minor and inconsistent variations identified which may have a variety of causes
A number of other factors can influence trip rates variation, such as location type, local population, public transport levels, etc

## Slide 5
OWEN EDWARDS
TRICS CONSORTIUM
TRICS
LOCATION TYPES

## Slide 6
OWEN EDWARDS
TRICS CONSORTIUM

## Slide 7
OWEN EDWARDS
TRICS CONSORTIUM
Looking at the largest survey sample possibilities results in three major location types to focus on
1 Town Centre/Edge of Town Centre
2 Suburban Area
3 Edge of Town

## Slide 8
OWEN EDWARDS
TRICS CONSORTIUM
LAND
USES

## Slide 9
OWEN EDWARDS
TRICS CONSORTIUM
Most popular land uses selected
01/A Food Superstore
02/A Office
03/A Houses Privately Owned

## Slide 10
OWEN EDWARDS
TRICS CONSORTIUM
01/A Food Superstore split into Friday only and Saturday only surveys
02/A Office and 03/A Houses Privately Owned will use only weekday surveys

## Slide 11
OWEN EDWARDS
TRICS CONSORTIUM
SELECTION
PARAMTERS

## Slide 12
OWEN EDWARDS
TRICS CONSORTIUM
As many surveys wanted to keep the samples as large as possible
Vehicles Only surveys
Looking at surveys from the past 20 years, minimum date set to 01/01/1999

## Slide 13
OWEN EDWARDS
TRICS CONSORTIUM
01/A FOOD SUPERSTORE FRIDAY RESULTS

## Slide 14
OWEN EDWARDS
TRICS CONSORTIUM
01/A FOOD SUPERSTORE FRIDAY
Results per 100m²
TRICS Location Types | Surveys (59) | Peak Totals (11.661)
3 Edge of Town | 26 | 12.542
2 Suburban Area | 20 | 11.510
1 Town Centre/Edge of Town Centre | 13 | 9.757

## Slide 15
OWEN EDWARDS
TRICS CONSORTIUM
01/A FOOD SUPERSTORE FRIDAY
Results per 100m²
TRICS Location Types | Surveys (59) | Trips Totals (139.976)
3 Edge of Town | 26 | 149.839
2 Suburban Area | 20 | 141.898
1 Town Centre/Edge of Town Centre | 13 | 102.822

## Slide 16
OWEN EDWARDS
TRICS CONSORTIUM
This sample shows Edge of Town with generally higher trip rates for both peak totals and trips totals
Town Centre/Edge of Town Centre shows generally lower trip rates for both peak totals and trips totals

## Slide 17
OWEN EDWARDS
TRICS CONSORTIUM
01/A FOOD SUPERSTORE SATURDAY RESULTS

## Slide 18
OWEN EDWARDS
TRICS CONSORTIUM
01/A FOOD SUPERSTORE SATURDAY
Results per 100m²
TRICS Location Types | Surveys (78) | Peak Totals (12.675)
3 Edge of Town | 34 | 13.396
2 Suburban Area | 28 | 12.007
1 Town Centre/Edge of Town Centre | 17 | 11.802

## Slide 19
OWEN EDWARDS
TRICS CONSORTIUM
01/A FOOD SUPERSTORE SATURDAY
Results per 100m²
TRICS Location Types | Surveys (78) | Trips Totals (142.637)
3 Edge of Town | 34 | 145.308
2 Suburban Area | 28 | 142.528
1 Town Centre/Edge of Town Centre | 17 | 120.902

## Slide 20
OWEN EDWARDS
TRICS CONSORTIUM
These data samples show a similar pattern of results to the 01/A Food Superstore Friday results
Edge of Town shows generally higher trip rates with Town Centre/Edge of Town Centre showing generally lower trip rates

## Slide 21
OWEN EDWARDS
TRICS CONSORTIUM
02/A OFFICE
WEEKDAY RESULTS

## Slide 22
OWEN EDWARDS
TRICS CONSORTIUM
02/A OFFICE WEEKDAY
Results per 100m²
TRICS Location Types | Surveys (130) | Peak Totals (0.734)
3 Edge of Town | 28 | 0.997
2 Suburban Area | 29 | 0.714
1 Town Centre/Edge of Town Centre | 73 | 0.601

## Slide 23
OWEN EDWARDS
TRICS CONSORTIUM
02/A OFFICE WEEKDAY
Results per 100m²
TRICS Location Types | Surveys (130) | Trips Totals (10.771)
2 Suburban Area | 29 | 11.813
3 Edge of Town | 28 | 11.222
1 Town Centre/Edge of Town Centre | 73 | 7.690

## Slide 24
OWEN EDWARDS
TRICS CONSORTIUM
Peak totals show a similar pattern of results to both 01/A Food Superstore sets of results
However, trips totals show Suburban Area having slightly higher trip rates than Edge of Town

## Slide 25
OWEN EDWARDS
TRICS CONSORTIUM
03/A HOUSES PRIVATELY OWNED WEEKDAY RESULTS

## Slide 26
OWEN EDWARDS
TRICS CONSORTIUM
03/A HOUSES PRIVATELY OWNED
Results per dwelling
TRICS Location Types | Surveys (192) | Peak Totals (0.595)
3 Edge of Town | 90 | 0.616
2 Suburban Area | 81 | 0.574
1 Town Centre/Edge of Town Centre | 21 | 0.560

## Slide 27
OWEN EDWARDS
TRICS CONSORTIUM
03/A HOUSES PRIVATELY OWNED
Results per dwelling
TRICS Location Types | Surveys (192) | Trips Totals (6.975)
3 Edge of Town | 90 | 7.102
1 Town Centre/Edge of Town Centre | 21 | 5.766
2 Suburban Area | 81 | 5.010

## Slide 28
OWEN EDWARDS
TRICS CONSORTIUM
Peak totals show a similar pattern of results to all 01/A Food Superstore and 02/A Office sets of results
Trips totals show Suburban Area having slightly lower trip rates than Town Centre/Edge of Town Centre

## Slide 29
OWEN EDWARDS
TRICS CONSORTIUM
CROSS LAND
USE RESULTS

## Slide 30
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Location Types | 01/AF | 01/AS | 02/AW | 03/AW
1 Town Centre/Edge of Town Centre | 3rd | 3rd | 3rd | 3rd
2 Suburban Area | 2nd | 2nd | 2nd | 2nd
3 Edge of Town | 1st | 1st | 1st | 1st
CROSS LAND USE RANKINGS
Based on Peak Totals (Ranked Highest to Lowest)

## Slide 31
OWEN EDWARDS
TRICS CONSORTIUM
CROSS LAND USE RANKINGS
Based on Trips Totals (Ranked Highest to Lowest)
TRICS Location Types | 01/AF | 01/AS | 02/AW | 03/AW
1 Town Centre/Edge of Town Centre | 3rd | 3rd | 3rd | 2nd
2 Suburban Area | 2nd | 2nd | 1st | 3rd
3 Edge of Town | 1st | 1st | 2nd | 1st

## Slide 32
OWEN EDWARDS
TRICS CONSORTIUM
Different land uses give reasonably similar results
Variation in rankings is minimal and strong consistencies are apparent

## Slide 33
OWEN EDWARDS
TRICS CONSORTIUM
Using the four data samples, it is possible to view each location type’s variance ranges from the average of all surveys
The two tables are based on total peak figures and total trips figures

## Slide 34
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Location Types | Surveys | High | Low | Average
1 Town Centre/Edge of Town Centre | 124 | -5.9% | -18.1% | -11.8%
2 Suburban Area | 158 | -1.3% | -5.3% | -3.2%
3 Edge of Town | 178 | +35.8% | +3.5% | +13.2%
TRIP GENERATION RANGES SUMMARY
Total Peak figures

## Slide 35
OWEN EDWARDS
TRICS CONSORTIUM
TRIP GENERATION RANGES SUMMARY
Total Trips figures
TRICS Location Types | Surveys | High | Low | Average
1 Town Centre/Edge of Town Centre | 124 | -15.2% | -28.6% | -21.9%
2 Suburban Area | 158 | +9.7% | -28.2% | -4.3%
3 Edge of Town | 178 | +7.0% | +1.8% | +3.7%

## Slide 36
OWEN EDWARDS
TRICS CONSORTIUM
The average variance tables show Edge of Town surveys have higher than average trip rates
Suburban Area surveys tend to have slightly lower than average trip rates
Town Centre/Edge of Town Centre have lower than average trip rates

## Slide 37
OWEN EDWARDS
TRICS CONSORTIUM
LOCATION TYPE TRIP RATES VARIATION FINDINGS

## Slide 38
OWEN EDWARDS
TRICS CONSORTIUM
These findings indicate location type variance produces a much more pronounced influence over trip rates than regional variance
The regional variance findings showed only minor and inconsistent variations which may have a variety of causes

## Slide 39
OWEN EDWARDS
TRICS CONSORTIUM
Location type results for each of the four land use category variations tended to produce similar results
This indicates location type can be one of the more significant factors when it comes to influencing trip rates

## Slide 40
OWEN EDWARDS
TRICS CONSORTIUM
TRIP RATES
INFLUENCES

## Slide 41
OWEN EDWARDS
TRICS CONSORTIUM
Instead of deselecting a region, ask why you have made a regional presumption about its trip rates
TRICS includes parameters for location type, local populations, public transport pass-bys, car ownership levels, etc

## Slide 42
OWEN EDWARDS
TRICS CONSORTIUM
FURTHER
WORK

## Slide 43
OWEN EDWARDS
TRICS CONSORTIUM
Following on from this second piece of research, the findings of both pieces will be combined to create a new Regional and Location Technical Note later this year